# HANDTOOL SAFETY TRAINING

# JIGSAW

- Training Safety Prerequisites

1)	Students are not permitted to use power tools while working alone

2)	All mains operated power tools must be of double insulated construction and be used in conjunction with an RCD device

3)	Suitable footwear that encloses and protects the foot

4)	Safety glasses are required

5)	Hearing protection and respirator may be necessary

6)	Wear appropriate clothing

8)	To prevent entanglement with moving parts, remove jewellery and tie back long hair

9)	Power extension leads must be located and run safely

- Risk Assessment of Jigsaw Operations

Jigsaws are commonly used in woodworking operations but may also be used to cut metal when the appropriate blades are fitted.  Typical injuries include electrocution, cuts, and eye injuries.

These injuries arise from using poorly maintained or damaged equipment, working in wet areas, not wearing safety glasses, not clamping work down or simply using the equipment outside of its operating parameters due to inexperience.

Students must be advised of the following risks and control measures associated with the operation of jigsaws.

| Task/Operation | hazard/injury | risk rating | control measure |
| --- | --- | --- | --- |
| Electrical testing & tagging current (annual) | Electrocution | Medium | Check that equipment has current tag |
| Visual electrical inspection | Electrocution | Medium | Ensure that leads, plugs and cable entries are undamaged |
| Fire and explosion | Injury to personnel and property | High | Electric drills are a ignition source – do not use around flammables or hydrogen |
| Checks | Eye and body injury | Medium | Ensure that correct blade is securely fitted for the material to be cut |
| Power Lead check | Electrocution | High | Check that power lead is not in the path of the blade |
| Cutting materials | Eye and body injury | High | Broken blades, material and work pieces can be ejected violently |
| Cutting materials | Inhalation of particles | High | Avoid exposure to airborne particles |
| Cutting materials | Cuts to fingers and body | High | Beware – most of the blade is not visible during cutting operations |
| Cutting materials | Accidental cuts | Medium | Overhang materials to be cut and check that no obstacles are present in cutting path |
| Operating speed | Blade may grab causing a torque reaction | Low | Ensure jigsaw speed is set correctly for the cutting task, especially metals |
| Operating pressure | Hand injury from breaking blade | Low | Do not use blunt blades or apply excessively high feed rates |
| Operating angle | Hand or body injury | Medium | Blade perpendicular to work to avoid grabbing or breaking |
| Operating position | All injuries | Low | Maintain a comfortable position with a balanced posture and a good view of the work |
| Operating position | All injuries | Low | Avoid using jigsaw in confined spaces |
| Withdrawing blade | All injuries | Low | Finish the cut, move blade back slightly from cut face, switch off jigsaw, then withdraw blade |
| Allen key | Impact injuries | High | Always removed blade changing key |
| After use | All injuries | Low | Always ensure jigsaw has stopped moving before putting down |
| After use | Injuries to other people | Medium | Unplug and leave on bench with blade removed |
| Blade replacement | All injuries | Low | Disconnect power before attempting to change blades |

- Training Assessment

When students have completed their safety training on the particular hand tool they will be required to demonstrate to the instructor that they can use it safely and proficiently and understand the specific risks associated with the operation.  They will then be authorised to use the equipment unsupervised.

Training assessments will be based on the following criteria:

1)	Student has been informed and understands the potential hazards and limitations associated with the hand tool and the situations in which it is used

2)	Student demonstrated basic competency in carrying out visual safety checks on the hand tool before using it

3)	Student demonstrated basic competency in changing cutting tools safely and selecting the correct operating speed

4)	Student has demonstrated the manual skills to hold and use the hand tool safely

- Safety Training Records

When Risk Assessment Section 2 and Training Assessment Section 3 are complete, ensure that students sign the accompanying Jigsaw Training Record (8c) that will be collected and returned to the Mechanical Administrative Office for filing.

This document remains valid for the duration of the student’s study in the Faculty.  All induction records will be retained for the duration of enrolment.