# HANDTOOL SAFETY TRAINING

# ROUTER

- Training Safety Prerequisites

1)	Students are not permitted to use power tools while working alone

2)	All mains operated power tools must be of double insulated construction and be used in conjunction with an RCD device

3)	Suitable footwear that encloses and protects the foot

4)	Safety glasses are required

5)	Hearing protection and respirator may be necessary

6)	Wear appropriate clothing

8)	To prevent entanglement with moving parts, remove jewellery and tie back long hair

9)	Power extension leads must be located and run safely

- Risk Assessment of Routing Operations

Portable routers operate with a high speed rotating cutter that can inflict a serious cut or amputation of small limbs.  In addition, this machine can jam, kick-back or dig-in causing a torque reaction that may cause an unprepared operator to be thrown off balance.  Potential injuries include electrocution, cuts, bruises and eye injuries.

These injuries arise from using poorly maintained or damaged equipment, working in wet areas, not clamping work down or simply using the equipment outside of its operating parameters due to inexperience.

Students must be advised of the following risks and control measures associated with the operation of routers.

| Task/Operation | hazard/injury | risk rating | control measure |
| --- | --- | --- | --- |
| Electrical testing & tagging current (annual) | Electrocution | Medium | Check that equipment has current tag |
| Visual electrical inspection | Electrocution | Medium | Ensure that leads, plugs and cable entries are undamaged |
| Changing cutting tool | All injuries | High | Always remove cutter tightening spanner |
| Fire and explosion | Injury to personnel and property | High | Electric routers are a ignition source – do not use around flammables or hydrogen |
| Non standard operation | Cuts, amputations | High | Never turn over router, fix to bench and use as a spindle moulding machine |
| Operating router | Cuts, amputations | High | Ensure that the correct guards or fences are fitted |
| Operating Router | Body injury due to loss of control | High | Never feed the cutter in the same direction as cutter rotation |
| Operating router | Eye and body injury | Medium | Broken tools, cutting debris and work pieces can be ejected violently |
| Operating router | Inhalation of particles | High | Avoid exposure to airborne particles even wood dust is harmful |
| Operating router | Cuts | Medium | Beware of sharp router tools |
| Operating speed | Cutter may grab causing a torque reaction | Low | If adjustable, ensure router speed is optimised for the task |
| Operating angle | Hand or body injury | Medium | Maintain cutter perpendicular to work to avoid grabbing |
| Operating position | All injuries | Low | Maintain a comfortable position, legs slightly apart and good view of the work |
| Operating position | All injuries | Low | Avoid using the router in confined spaces |
| Changing cutting tool | All injuries | Low | Always disconnect power before changing cutting tool |
| After use | All injuries | Low | Always ensure router has stopped rotating before putting down |
| After use | Injuries to other people | Medium | Unplug and leave on bench with cutter removed |
| Cutter replacement | Cuts, amputations | High | Disconnect power before attempting to change cutters |

3.	Training Assessment

When students have completed their safety training on the particular hand tool they will be required to demonstrate to the instructor that they can use it safely and proficiently and understand the specific risks associated with the operation.  They will then be authorised to use the equipment unsupervised.

Training assessments will be based on the following criteria:

1)	Student has been informed and understands the potential hazards and limitations associated with the hand tool and the situations in which it is used

2)	Student demonstrated basic competency in carrying out visual safety checks on the hand tool before using it

3)	Student demonstrated basic competency in changing cutting tools safely and selecting the correct operating speed

4)	Student has demonstrated the manual skills to hold and use the hand tool safely

4.	Safety Training Records

When Risk Assessment Section 2 and Training Assessment Section 3 are complete, ensure that students sign the accompanying Router Training Record (8c) that will be collected and returned to the Mechanical Administrative Office for filing.

This document remains valid for the duration of the student’s study in the Faculty.  All induction records will be retained for the duration of enrolment.