INTRODUCTION TO MACHINING (3-JAW CHUCK)

SAFETY CHECKLIST

- Laboratory Safety Prerequisites

- Student to technician ratio does not exceed 3:1

2)	The safety and machine instruction process takes into account language barriers.

- Students are shown were to store their bags in order to maintain unobstructed

walkways

- Students have attended the Manufacturing 208 Lecture prior to attending the workshop.  If this has not been carried out they may not proceed

- Suitable footwear that encloses and protects the foot

- Safety glasses

- Appropriate clothing

- Long hair is tied back

- Removal of all jewellery that is likely to become caught in machinery

- Students are informed of the Emergency Evacuation Procedure

- Students are advised of the nearest fire extinguisher and suitability for fighting a fire where machinery and electrical hazards are present

- Students are advised of the First Aid facilities, the nearest First Aid Officer and the position of the emergency phone and emergency numbers

- Students are shown the position of the Emergency Stop Button and advised of the circumstances for its use.

- Risk Assessment of Machining Operations

Students must be advised of the following risks and control measures associated with the machining task they will be performing.

| Task/Operation | hazard/injury | risk rating | control measure |
| --- | --- | --- | --- |
| While in G27 | Eye injury | High | Wearing safety glasses |
| While in G27 | Foot injury | Medium | Enclosed footwear |
| While in G27 | Hair caught in machine | Medium | Long hair tied back at all times |
| Chuck key safety check | Projectile injury | High | Check before starting machine |
| Turning lathe on/off | Accidental activation injury | High | Familiarity with this operation |
| Using foot brake | Response to any injury | N/A | Familiarity with this operation |
| Maintaining safe operating zone | Injury from rotating and cutting elements | High | Always keep body parts at a safe distance from machine elements |
| Handling drill bits and sharp tools | Cuts | Low | Hold drills and tools at the base to prevent cuts |
| Securing drills and tools | Projectile injury | High | Check that drill is locked in place and not wound past 30 mm |
| Drilling holes | Eye or face injury | Medium | Ensure that drill is removed before bending over the machine |
| Maintaining safe swarf length | Cuts from swarf | Medium | Release drill/tool pressure |
| Positioning work-piece | Injury from collision of cutting tool and chuck | High | Position work-piece in chuck and ensure correct distance with reference to notes |
| Securing work-piece | Projectile injury | High | Tighten chuck to ensure work-piece is secure |
| Rotating chuck | Injury from unattended, rotating chuck | High | Always disengage chuck when leaving machine unattended |
| Securing tool post | Injury from accidental movement of cutting tool | Medium | Check tool post is secure, tighten if necessary |
| Maintaining a safe chuck speed | Projectile injury | High | Familiarity with this operation |

| Position of tool post and tool when lathe is started | Projectile injury | High | Ensure tool is clear of chuck rotation before starting |
| --- | --- | --- | --- |
| Compressed air | Eye injury and skin penetration of jet | High | Use with care and only when necessary |
| Deburring work piece | Cuts from sharp edges | Medium | Ensure the work piece is securely held |
| Application of coolant | Contact with rotating chuck | Medium | Use jet on applicator and keep a safe distance |

- Safety Training Records

When Risk Assessment Section 2 is complete, ensure that students sign the accompanying 3-Jaw Chuck Safety Training Record that will be collected and returned to the Mechanical Administrative Office for filing.

- Supervision and Instruction of Machining Operations

Students are to be supervised for the duration of the Introduction to Machining class and will receive practical instruction as they proceed.  This instruction will reinforce the safety hazards of the specific operations identified in Section 2.

This document remains valid for the duration of the Machining Laboratory.  All training records will be retained in file F9 for the duration of enrolment.