WORKSHOP PRACTICE (DRILLING, TAPPING & FILING)

SAFETY CHECKLIST

- Laboratory Safety Prerequisites

- Student to technician ratio does not exceed 4:1

- Students are shown were to store their bags in order to maintain unobstructed

walkways

- Students have attended the Manufacturing 208 Lecture prior to attending the workshop.  If this has not been carried out they may not proceed

- Suitable footwear that encloses and protects the foot

- Safety glasses

- Appropriate clothing

- Long hair is tied back

- Removal of all jewellery that is likely to become caught in machinery

- Students are informed of the Emergency Evacuation Procedure

- Students are advised of the nearest fire extinguisher and suitability for fighting a fire where machinery and electrical hazards are present

- Students are advised of the First Aid facilities, the nearest First Aid Officer and the position of the emergency phone and emergency numbers

- Students are shown the position of the Emergency Stop Button and advised of the circumstances for its use

- The safety and machine instruction process takes into account language barriers.

- Risk Assessment of Machining Operations

Students must be advised of the following risks and control measures associated with the machining task they will be performing.

| Task/Operation | hazard/injury | risk rating | control measure |
| --- | --- | --- | --- |
| While in G27 | Eye injury | High | Wearing safety glasses |
| While in G27 | Foot injury | Low | Appropriate footwear |
| While in G27 | Hair caught in machine | High | Long hair tied back |
| Chuck key safety check | Projectile injury | Medium | Check before starting machine |
| Drilling material | Injury from rotating material due to drill bit jamming in hole | Medium | Prevent vice from rotating, use stop or clamp where appropriate |
| Drilling material | Injury from shattered drill bit | Medium | Demonstrate correct drill feed rate, do not feed too fast |
| Maintaining safe swarf length | Cuts from swarf | High | Control length of swarf by modulating drill pressure |
| Compressed air | Eye injury | Medium | Use a brush instead of air to remove debris |
| Handling drill bits and sharp tools | Cuts | Low | Hold drills and tools at the base to prevent cuts |
| Hitting the centre punch | Hitting hand with hammer | Low | Demonstrate the correct method |
| Marking out/drilling | Cuts from sharp edges of material | Low | Inform students of the risk |

3.	Safety Checklist Records

When Risk Assessment Section 2 is complete, ensure that students sign the accompanying Workshop Practice  Safety Training Record that will be collected and returned to the Mechanical Administrative Office for filing.

- Supervision and Instruction of Machining Operations

Students are to be supervised for the duration of the Marking and Drilling class and will receive practical instruction as they proceed.  This instruction will reinforce the safety hazards of the specific operations identified in Section 2.

This document remains valid for the duration of the Machining Laboratory.  All training records will be retained in file F9 for the duration of enrolment.