# HANDTOOL SAFETY TRAINING

# ANGLE GRINDER (100 mm disc size only)

- Training Safety Prerequisites

1)	Students are not permitted to use power tools while working alone

2)	All mains operated power tools must be of double insulated construction and be used in conjunction with an RCD device

3)	Suitable footwear that encloses and protects the foot

4)	Safety glasses and full face shield for the operator

5)	Hearing protection

6)	Appropriate clothing, gloves and respirator may be necessary

7)	To prevent entanglement with moving parts, remove jewellery and tie back long hair

8)	Power extension leads must be located and run safely

- Risk Assessment of Machining Operations

Angle grinders are one of the most dangerous tools in any workplace.

Most angle grinder injuries are from metal particles lodging in the operator's eye.

However the most serious injuries are from kick-back, where the disc is thrust back violently towards the operator.

Discs can shatter or explode, sending pieces flying in all directions.

Because angle grinders are designed for grinding and not for cutting, the use of cutting discs with angle grinders exposes operators to even greater risks.

WorkSafe Western Australia says:

Where a safer alternative cutting tool is available or can be obtained . . .

AN ANGLE GRINDER SHOULD NOT BE USED AS A CUTTING TOOL.

Students must be advised of the following risks and control measures associated with the operation of angle grinders.

| Task/Operation | hazard/injury | risk rating | control measure |
| --- | --- | --- | --- |
| Disc safety check | Eye and body injury from disc shattering | High | Cutting discs should not be used for grinding jobs and visa versa |
| Disc rotation speed check | Eye and body injury from disc shattering | High | Ensure grinder speed is compatible with disc speed rating |
| Disc type check | Eye and body injury from disc shattering | High | Type of disc used must be compatible with the operation and the material |
| Disc wear check | Eye and body injury from disc shattering | High | Discard worn discs and never use on smaller grinders |
| Guard and handle check | Eye injury and cuts | High | Guard and handle securely in place and guard covers half the disc |
| Flange and locking nut check | Eye and body injury from disc shattering | High | Correct flange and locking nut for the disc used |
| Check for damage and defects in disc | Eye and body injury from disc shattering | High | Discard damaged or worn out discs |
| Check for dropped or wet discs | Eye and body injury from disc shattering | High | Discard any affected discs |
| Electrical testing & tagging current (annual) | Electrocution | Medium | Check that equipment has current tag |
| Visual electrical inspection | Electrocution | Medium | Ensure that leads, plugs and cable entries are undamaged |
| Fire and explosion | Injury to personnel and property | High | Grinding is an ignition source – especially for hydrogen |
| Grinder orientation | Eye and body injury | High | Ensure side handles are set up for right or left handed operation |
| Operating speed | Eye and body injury from disc shattering | Medium | Ensure grinder has run up to full speed before using |
| Operating pressure | Eye and body injury from disc shattering | High | Avoid ‘dig-in’ and ‘kick-back’ by applying minimum pressure to disc |
| Disc impacts | Eye and body injury from disc shattering | High | Avoid impacting disc onto the job or striking other objects |
| Operating angle | Eye and body injury from disc shattering | High | Maintain a 15 to 30 degree angle to the work |
| Operating position | Eye and body injuries | Medium | Maintain a comfortable position, legs slightly apart and good view of the work |
| Operating position | Body injuries | Medium | Never use the grinder between the legs |
| Operating position | Eye and body injuries | Medium | Always operate grinder at waist height with both hands |
| Disc replacement | Eye and body injuries | High | Disconnect power before attempting to change disc |
| After use | Body injuries | Medium | Always ensure disc has stopped rotating before putting down |
| After use | Injuries to other people | Medium | Unplug and leave on bench with disc facing up |

- Training Assessment

When students have completed their safety training on the particular hand tool they will be required to demonstrate to the instructor that they can use it safely and proficiently and understand the specific risks associated with the operation.  They will then be authorised to use the equipment unsupervised.

Training assessments will be based on the following criteria:

1)	Student has been informed and understands the potential hazards and limitations associated with the hand tool and the situations in which it is used

2)	Student demonstrated basic competency in carrying out visual safety checks on the hand tool before using it

3)	Student demonstrated basic competency in changing cutting tools safely and selecting the correct operating speed

4)	Student has demonstrated the manual skills to hold and use the hand tool safely

- Safety Training Records

When Risk Assessment Section 2 and Training Assessment Section 3 are complete, ensure that students sign the accompanying Angle Grinder Training Record (8c) that will be collected and returned to the Mechanical Administrative Office for filing.

This document remains valid for the duration of the student’s study in the Faculty.  All induction records will be retained for the duration of enrolment.