JIGSAW

SAFETY INSTRUCTIONS

These safety instructions are provided to students as a reference to remind them of the specific safety issues and safe operating procedures training they have received for using Jigsaws.

1.	Training Safety Prerequisites

1)	Students are not permitted to use power tools while working alone

2)	All mains operated power tools must be of double insulated construction and be used in conjunction with an RCD device

3)	Suitable footwear that encloses and protects the foot

4)	Safety glasses

5)	Depending on the work hearing protection may be necessary

6)	Appropriate clothing

7)	Depending on the work a respirator may be necessary

8)	To prevent entanglement with moving parts, remove jewellery and tie back long hair

9)	Power extension leads must be located and run safely

2.	Risk Assessment of Machining Operations

Jigsaws are commonly used in woodworking operations but may also be used to cut metal when the appropriate blades are fitted.  Typical injuries include electrocution, cuts, and eye injuries.

These injuries arise from using poorly maintained or damaged equipment, working in wet areas, not wearing safety glasses, not clamping work down or simply using the equipment outside of its operating parameters due to inexperience.

All students should be aware of the following risks and control measures associated with the operation of portable drills.

3.	Electrical Checks

1)	Electrical testing and tagging – do not use electrical appliances in the University that do not have a current tag.

2)	Visual electrical check – visually check the electrical appliance for signs of damage, especially to lead, plugs and cable entries.  Damaged electrical appliances can cause death or serious injury.

4.	Pre-operational Checks

1)	Allen key check – ensure that the blade removal key has been removed from the equipment before operation.

2)	Ignition source – all electrical hand tools produce sparks at the commutator, ensure that the jigsaw is not used in a location where explosive gasses are present.

3)	Blade check – jigsaws can be used for a variety of cutting tasks with wood and metal.  It is important to ensure that correct blade is securely fitted for the material to be cut.  Do not use blunt or damaged blades.

4)	Cutting speed – ensure that the jigsaw speed is set to the optimum speed for the job and the material being used.

4)	Power cable check – the operation of a jigsaw involves the cutting blade being out of sight on the underside of the material.  Check that the power cable is well clear of the cutting path.

5.	Operation

1)	Eye injuries – Broken blades, material and work pieces can be ejected violently.  It is important to wear eye protection.

2)	Cutting materials – avoid breathing airborne particles from the material being cut; in particular wood dust.

3)	Cutting materials – avoid cuts to the fingers and body that may occur from not being able to see the cutting blade.

4)	Positioning material – it is preferable to overhang the section of material that needs to be cut and ensure that there is an obstacle free path for the height of the blade.

5)	Operating pressure – the operating pressure will determine the feed rate.  Do not use excessive pressure for high feed rates since this may result in the blade grabbing or breaking.

6)	Jigsaw orientation – try to maintain the alignment of the blade perpendicular to the job surface.  Incorrect angle may result in the blade grabbing or breaking.

7)	Operating position – always maintain a comfortable operating position with a balanced posture and body bent slightly forward to maintain a good view of the cutting line.  Do not use the jigsaw in a confined position, especially when the position of the blade is not known.

8)	Withdrawing blade – it is important to use this sequence otherwise the blade may jam or snap.  Finish the cut and move the blade back slightly from the cutting face – switch off the jigsaw and withdraw the blade when it has stopped moving.

9)	Blade release key – always remove the blade release key before switching on the jigsaw, otherwise serious projectile injuries can occur.

6.	On Completion of Work

1)	Putting the jigsaw down – always ensure that the jigsaw has stopped moving before it has been put down, otherwise the blade may become entangled with other materials.

2)	Blade replacement – always disconnect the power before changing or removing the blade to prevent serious cuts from the equipment being accidentally turned on.

2)	Disconnection – always unplug the jigsaw from the power when it is not in use and remove the blade.  Store the jigsaw in a protected dry place to prevent damage to the equipment.

.